## Slide 1
Can the rail network absorb the America's Cup?
Part B — Capacity & Saturation analysis (V/C). Diagnosis only; mitigation = Services-improvement section.
Headline: NOT a capacity problem — a DISTRIBUTION problem.
• Metro Line 1 is the binding constraint: 0.69 → 0.84 at peak, >1.0 if transit share hits 60%.
Demand growth into event zones:
• Region-wide +11%
• Central event zones +23%
• Napoli Centrale gateway +50%
• The race venue (Bagnoli) is over-served — 3 lines, V/C only ~0.35.
Notes: 30s: I analysed whether the rail network can absorb the America's Cup demand with a V/C saturation analysis. Key finding: not a total-capacity problem, a distribution problem. The Bagnoli venue has 3 lines and spare capacity, but Metro Line 1 — the central spine through Napoli Centrale — is the binding constraint: 0.69 to 0.84 at peak, over 1.0 if transit share reaches 60%. So the network won't collapse overall, but L1 will unless that corridor is reinforced.

## Slide 2
Saturation concentrates on the central spine — not the venue
• Venue (West): 3 lines, V/C ~0.35 — ample headroom. Central spine L1: 0.69→0.84, crosses 1.0 at 60% transit share.
Notes: Two angles. Left: spatial — red bubbles (big tourist load, saturated) cluster in central Naples / Napoli Centrale; green = the venue, which has headroom. Right: sensitivity — I tested transit share at 40/50/60% because the phone data can't observe metro mode share. Only Line 1 crosses 1.0, and only at 60%. So the conclusion 'L1 is the constraint' is robust to the assumption; the absolute number isn't, and I'm transparent about that.

## Slide 3
Where demand comes from (OSRM) + conclusion
Road accessibility (my OSRM 222×222 real-road time matrix):
• 73% of Campania-origin tourist demand is within a 45-min drive (mean 37 min) → Naples-centred → confirms central L1 pressure.
• ~20% comes from >60 min away (Salerno/Cilento) → relies on road approaches + regional rail.
Conclusion
• Total capacity is sufficient (~24,000 pax/h/dir) — the issue is its distribution.
• → Target relief on L1 / Napoli Centrale (peak frequency ↑, divert via Line 6 Municipio↔Mostra).
• Concrete measures (shuttle bus) → Services-improvement section.
Notes: I also built a real road-network travel-time matrix with OSRM to see where demand originates. 73% is within a 45-min drive of the venues — Naples-centred, which is exactly why the central Line 1 corridor takes the pressure. ~20% comes from beyond 60 min and leans on regional rail. Conclusion: it's a distribution problem, not a shortfall — target Line 1 and the gateway, rather than building new lines. The detailed mitigation (shuttle bus) is the Services-improvement part.